## Slide 1
Enhanced environmental protection inspection for efficient control of air quality monitoring and of all entities under obligation within system of greenhouse gas emission allowance trading, in order to achieve better air quality in Republic of Croatia
This project is funded by the European Union

## Slide 2: 13. Croatian regulation reporting
Energy research and Environmental Protection Institute
Bojan Abramović dipl. ing. stroj.
Predrag Hercog, dipl. inž. medicinske biokemije

## Slide 3: 13.1 DATA REQUIRED TO SUBMIT
Air protection information system
  integral part of the Environmental protection information system that is conducted under the Environmental Protection Act that forms part of the European environmental information system
  http://iszo.azo.hr/Pretraga_TS.aspx
Air protection information system is run by the Croatian Environment and Nature Agency and supervised by the Ministry (competent authority) and includes:
  http://www.azo.hr/BazePodataka03
  air quality data from the state network,
  air quality data from measuring stations of local and local government units and measurements of special purpose provided by the polluter,
  plans and programs for the protection and improvement of air quality,
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia

## Slide 4: 13.1 DATA REQUIRED TO SUBMIT
Air protection information system contains (continued):
  alert thresholds and information threshold exceeding data and measures for human health and environment protection on such occasions,
  data on legal entities carrying out the activity of air quality monitoring, emission monitoring of pollutants in air from immovable sources, accuracy verification of the measuring system for continuous measurement of pollutant emissions from the immovable sources and quality assurance of air quality measurement and data,
  performed inspection data,
  committed offenses information,
  other data important for the air protection, ozone layer, climate change mitigation and adaptation to climate change
  ……
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia

## Slide 5: 13.1 DATA REQUIRED TO SUBMIT
Air protection information system contains (public and data connectivity...):
  The central state administration bodies and local and regional government units, legal entity with public authority, are obliged to submit, in a timely manner and without compensation, the information from their jurisdiction required for the air protection information system management and for the preparation of the Plan, Program and Reports .
  The air protection information system is aligned and linked to the information systems run by other state administration bodies, local and regional government units and legal entity with public authority.
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia
  http://www.zzjzpgz.hr/zrak/
  http://zrak.zzjziz.hr/
  http://www.mzoip.hr/hr/inspekcija/izvjesca-.html

## Slide 6: 13.1 DATA REQUIRED TO SUBMIT
Air protection information system contains (public and data connectivity...):
  link to the Air quality portal in Croatia is also available on the Central State Portal on Air quality
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia
  - https://www.gov.hr/moja-uprava/stanovanje/briga-o-okolisu/kvaliteta-zraka/488

## Slide 7: 13.1 DATA REQUIRED TO SUBMIT
Air protection information system contains (public and data connectivity...):
  Government authourity, local and regional government and legal entity with public authority possessing information relevant to air quality management and the management of the Air Information System shall be obliged to submit or make available to the Agency in electronic form at its request. (Air Protection Act, Article 119.)
  The owner and/or user becomes responsible for monitoring the air quality established in the state network and in the counties, towns and cities and in accordance with the decision on the acceptability of the environmental project or the solution on the integrated environmental protection conditions, is obliged to ensure a continuous transfer of source and validated data for pollutants whose concentration in the air is determined by automatic measuring instruments for the computer network in air quality information system using the protocols and formats defined by the Agency. (Ordinance on Air Quality, Article 21. )
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia

## Slide 8: 13.2 DATA SUBMITTED TO THE AGENCY DATABASE
Air quality portal
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia
http://iszz.azo.hr/iskzl/index.html

## Slide 9: 13.2 DATA SUBMITTED TO THE AGENCY DATABASE
Data on the Air Quality Portal or the Agency database are:
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia
  Current and validated values ​​of concentrations of pollutants in the air - statistical data, exceeded limit values and target values, alert thresholds and warning thresholds ....
  Network and Station informations (metadata)
  Annual reports on air quality monitoring
  Action Plans and Action plans data submitted to the EC
  Users also have access to static browsers, exceeding limit and target values, and trends; data are presented in tabular and graphical terms and can be downloaded (web services)

## Slide 10: 13.2 DATA SUBMITTED TO THE AGENCY DATABASE
Air quality portal
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia
  Network and Station information (metadata)
  http://iszz.azo.hr/iskzl/index.html
  Local Network State Network

## Slide 11: 13.2 DATA SUBMITTED TO THE AGENCY DATABASE
Air Quality Portal in Croatia - Annual reports on air quality monitoring
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia
  Annual reports in Croatia (prepared by Agency, national and local networks)
  http://iszz.azo.hr/iskzl/godizvrpt.htm?pid=0&t=0
  Annual State Network Reports
  http://iszz.azo.hr/iskzl/godizvrpt.htm?pid=0&t=1
  Annual Local Area Network Reports
  http://iszz.azo.hr/iskzl/godizvrpt.htm?pid=0&t=2

## Slide 12: 13.2 DATA SUBMITTED TO THE AGENCY DATABASE
Air Quality Portal in Croatia - Annual reports on air quality monitoring
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia
  Annual reports in Croatia (prepared by Agency, national and local networks)
  http://iszz.azo.hr/iskzl/godizvrpt.htm?pid=0&t=0

## Slide 13: 13.2 DATA SUBMITTED TO THE AGENCY DATABASE
Air Quality Portal in Croatia - Annual reports on air quality monitoring
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia
  Annual reports in Croatia (prepared by Agency, national and local networks)
  http://iszz.azo.hr/iskzl/godizvrpt.htm?pid=0&t=0

## Slide 14: 13.2 DATA SUBMITTED TO THE AGENCY DATABASE
Air Quality Portal in Croatia:
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia
  Action Plans
  http://iszz.azo.hr/iskzl/godizvrpt.htm?pid=0&t=4

## Slide 15: 13.2 DATA SUBMITTED TO THE AGENCY DATABASE
Air Quality Portal in Croatia:
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia
  data on action plans submitted to EC
  http://iszz.azo.hr/iskzl/hPlan.htm

## Slide 16: 13.2 DATA SUBMITTED TO THE AGENCY DATABASE
Air Quality Portal in Croatia:
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia
  Data (surce and validated)
  http://iszz.azo.hr/iskzl/podatak.htm

## Slide 17: 13.2 DATA SUBMITTED TO THE AGENCY DATABASE
Air Quality Portal in Croatia:
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia
  Data (sourse and validated), statistical data, data on limit values and target values, notification thresholds and warning thresholds ....
  http://iszz.azo.hr/iskzl/index.html

## Slide 18: 13.3 REPORT ON THE BASIS OF THE INFORMATION AND ALERT THRESHOLD
The alert threshold for SO2 and NO2 and the information threshold for ozone are set out in Annex 5 to the Regulation on levels of pollutants in the air (NN 117/12).
If the alert threshold for SO2 and NO2 and the information threshold and alert threshold for ozone have been exceeded in an area - the public is notified according to the Regulation on levels of pollutants in the air.
If the alert threshold for SO2 and NO2 and the information threshold or alert threshold for ozone have been exceeded in the state border area, the Croatian competent authority will notify the competent authority of the neighboring state.
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia

## Slide 19: 13.3 REPORT ON THE BASIS OF THE INFORMATION AND ALERT THRESHOLD
Alert threshold for pollutants other than ozone:
To exceed the alert threshold, it shall be measured for three consecutive hours at locations representative places of air quality over at least 100 km2, or in entire zone or agglomeration, whichever is the smaller.
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia
Pollutant | Alert threshold
Sulphur dioxide SO2 | 500 µg/m3
Nitrogen dioxide NO2 | 400 µg/m3

## Slide 20: 13.3 REPORT ON THE BASIS OF THE INFORMATION AND ALERT THRESHOLD
Information and alert thresholds for ozone:
For the application of Article 47. (short-term action plans) of the Air Protection Act, threshold exceedance is to be measured or predicted for three consecutive hours.
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia
Purpose | Averaging period | Threshold
Information | 1 hour | 180 µg/m3
Alert | 1 hour | 240 µg/m3

## Slide 21: 13.3 REPORT ON THE BASIS OF THE INFORMATION AND ALERT THRESHOLD
Specific measures for human health and environment protection in case of exceeding the alert and information threshold:
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia
  In the avent of information threshold being exceeded for SO2 and NO2 and of alert and information threshold being exceeded for ozone, the executive body of the local government in whose territory thresholds being exceeded is required to take specific measures for the human health and environment protection prescribed in Annex 6 to the Regulation on levels of pollutants in the air (NN 117/12) and to determine the manner of their implementation according to a special act regulating the prevention of major accidents involving hazardous substances.
  The executive body of the local government is obliged to report an alert and information threshold to ensure media coverage through the media several times throughout the day.
  The executive body of the local government through the media announces the end of the exceeding an alert and information threshold

## Slide 22: 13.3 REPORT ON THE BASIS OF THE INFORMATION AND ALERT THRESHOLD
SO2 and NO2 alert threshold exceedance and information and alert threshold for ozone in the air
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia
  the executive body of the local government in whose territory thresholds being exceeded shall be obliged to inform the public in a timely manner of detailed information on all current or predicted exceedances of alert and inforamation threshold

## Slide 23: 13.3 REPORT ON THE BASIS OF THE INFORMATION AND ALERT THRESHOLD
Detailed data includes the following:
data on recorded overdraft
forecast for the following afternoon / day (days):
  geographic area where the alert and information threshold is exceeded,
  expected changes in pollution (improvement, stabilization or deterioration), together with the reasons for such changes;
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia
  place or area of exceeding
  the type of threshod being exceeded
  start time and duration of exceeding
  the highest one-hour concentration and, in the case of ground-level ozone, the highest ozone average concentration;

## Slide 24: 13.3 REPORT ON THE BASIS OF THE INFORMATION AND ALERT THRESHOLD
Detailed data (continued):
population data that is exposed, possible effects on health and recommended behavior:
  data on affected population groups,
  description of possible symptoms,
  the recommended precautionary measures that the exposed population should undertake,
  where to find further information;
data on preventive procedures for pollution reduction and / or exposure to pollutants: guidance of the sector with major sources of pollution; recommendations for emission reduction procedures.
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia

## Slide 25: 13.3 REPORT ON THE BASIS OF THE INFORMATION AND ALERT THRESHOLD
Specific measures for human health and environment protection in case of exceeding the alert and information threshold:
  Warnings and advices to the population:
  invite the population to take care that their behavior and activities would not contribute to air pollution further and endanger the affected populations groups
  recommend that fossil fuels are not used for heating rooms, especially those without efficient exhaust fumes,
  for cooking use wherever possible electric cookers and ovens instead of gas stoves and solid fuel stoves,
  do not smoke in the living and working areas
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia

## Slide 26: 13.3 REPORT ON THE BASIS OF THE INFORMATION AND ALERT THRESHOLD
  Warnings and advices to the population (continued):
  postpone cleaning with agents containing corrosive chemicals and solvents, repairs using adhesives, paints, varnishes, insecticide use and all other activities and activities that are not urgent and necessary and which pollute the air in the rooms as the rooms can not to open the window,
  recommend that mechanical ventilation is not used to inject air into the room and not open the windows,
  recommend that small children, pregnant women, elderly people, chronic patients, people with poor health, and vulnerable persons at critical times do not go out into the street
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia

## Slide 27: 13.4 ANNUAL REPORTS
For each permanent measurement site established in the counties, the City of Zagreb and cities and in accordance with the decision on the acceptability of the environmental project or the solution on the integrated environmental protection conditions, legal entity - test laboratory,
- http://iszz.azo.hr/iskzl/godizvrpt.htm?pid=0&t=2
For each measurement site from the State Air Quality Monitoring Network, the reference laboratories must produce an Air quality monitoring report for each calendar year.
- http://iszz.azo.hr/iskzl/godizvrpt.htm?pid=0&t=1
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia

## Slide 28: 13.4 ANNUAL REPORTS
The annual reports on air quality monitoring must include information on:
  legal entity - a test laboratory or a reference laboratory performing air quality monitoring
  measurement site for sampling and measurement range
  time and sampling
  used measurement methods and the used measuring equipment
  ensuring the quality of data according to the requirements of the harmonized standards for test and calibration laboratories
  other quality assurance data, such as ensuring continuity, participation in comparative measurements, deviations from the prescribed methodology and the reasons for this.
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia

## Slide 29: 13.4 ANNUAL REPORTS
The annual reports for each pollutant include the following data:
  about the level of air pollution and the dates and times of air pollution exceeding the limit values, target values ​​and long-term goals for ground-level ozone
  exceeding alert and information thresholds, as well as dates and times
  calculated statistical air pollution parameters for pollutants according to the standards set out in Appendix 8. Air Quality Monitoring Ordinance - arithmetic center, cedium, relevant percentage and maximum value, include data - percentage of total possible number of data and number of data for relevant averaging times
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia

## Slide 30: 13.4 ANNUAL REPORTS
The annual reports for each pollutant include the following dana (continued):
  average annual value of ozone precursors, polycyclic aromatic hydrocarbons and chemical composition in leachate PM2.5 particles
  level of air pollution in relation to the upper and lower estimate thresholds
  criteria used for assessing air pollution (LV, CV, DC, DPP, GPP, PU, ​​PO ...)
  causes of exceeding limit value, target value and long-term goal for ozone
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia

## Slide 31: 13.4 ANNUAL REPORTS
According to the levels of pollution, given the required limit values ​​(LV), the target values ​​and the target values ​​for ozone are determined by the following air quality categories:
- the first category of air quality - clean or slightly polluted air: not exceeding the limit value (GV), target values ​​and target values ​​for ozone,
- the second category of air quality - polluted air: limit values ​​(LV), target values ​​and target values ​​for ozone have been exceeded.
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia

## Slide 32: 13.4 ANNUAL REPORTS
The air quality categories in the paragraph are determined for each pollutant separately and refer to the protection of human health, the quality of life, the protection of vegetation and the ecosystem.
The air quality categories are determined once a year for the previous calendar year.
The annual air quality monitoring report on the territory of the Republic of Croatia with the list of air quality categories is made by the Agency and published on the web site.
- http://iszz.azo.hr/iskzl/godizvrpt.htm?pid=0&t=0
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia

## Slide 33: 13.4 ANNUAL REPORTS
Air quality categories - examples from the Agency's report
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia

## Slide 34: 13.4 ANNUAL REPORTS
Air quality categories - examples from the Agency's report
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia

## Slide 35: 13.4 ANNUAL REPORTS
Total number of categorized measuring point in the year 2014. and 2015. with number I and II category for each pollutant - Agency's report
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia

## Slide 36: 13.4 ANNUAL REPORTS
Measurement sites by zones and agglomerations where air was the 2nd category for all pollutants in a year 2015.
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia

## Slide 37: 13.4 ANNUAL REPORTS
Measurement sites - agglomerations on which air was the 2nd category for all pollutants in a year 2015.
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia

## Slide 38: 13.4 ANNUAL REPORTS
Measurement sites - the zones where the air was 2nd category for all pollutants in a year 2015.
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia

## Slide 39: 13.4 ANNUAL REPORTS
Based on the reports, the Agency produces an annual report on air quality in the Republic of Croatia
  for at least measurement sites for the monitoring of sulfur dioxide, nitrogen oxides, particulate matter (PM10 and PM2,5), lead, benzene, carbon monoxide, ozone and ozone precursors, arsenic, cadmium, mercury, nickel, benzopyrene and other polycyclic aromatic hydrocarbons in air used for the mutual exchange of information and reporting on air quality between the Agency and the European Commission,
  can be made as needed for other measurement site and contain other data as needed
http://iszz.azo.hr/iskzl/godizvrpt.htm?pid=0&t=0
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia

## Slide 40: 13.4 ANNUAL REPORTS
The Agency’s report contains:
  air pollution assessment by pollutants for each zone and agglomeration
  summary levels that exceed the limit values, target values, long-term goals, information thresholds and alert thresholds for relevant times. This data is combined with a summary assessment of the exceeding effects
  additional data and estimates of forest protection when available, as well as data on other pollutants for which the monitoring provisions set out in this Regulation, such as, inter alia, some ozone precursors that are not regulated by regulations and which are listed in the Regulation on Levels.
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia

## Slide 41: 13.4 ANNUAL REPORTS
The Agency’s report - air pollution assessment by pollutants for each zone and agglomeration (examples)
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia

## Slide 42: 13.4 ANNUAL REPORTS
The Agency’s report - air pollution assessment by pollutants for each zone and agglomeration (examples)
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia

## Slide 43: 13.4 ANNUAL REPORTS
The Agency’s report - summary levels exceeding threshold values, target values, long-term goals, information thresholds and warning thresholds, for relevant mediation times (examples)
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia

## Slide 44: 13.4 ANNUAL REPORTS
The Agency’s report - summary levels exceeding threshold values, target values, long-term goals, information thresholds and warning thresholds, for relevant mediation times (examples)
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia

## Slide 45: 13.4 ANNUAL REPORTS
The Agency’s report - summary levels exceeding threshold values, target values, long-term goals, information thresholds and warning thresholds, for relevant mediation times (examples)
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia

## Slide 46: 13.4 ANNUAL REPORTS
The Agency submits to the Ministry (competent authority) an annual report on the territory of the Republic of Croatia by September 30th of the current year for the previous calendar year and publishes it on its web site.
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia

## Slide 47: 13.4 DATA SUBMISSION DYNAMICS
State Network - The National Hydrometeorological Institute submits to the Ministry and Agency original and validated data and air pollution reports on levels and quality assessment by April 30th of the current year for the previous calendar year.
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia

## Slide 48: 13.4 DATA SUBMISSION DYNAMICS
Local Networks (JRS and JLS)
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia
  The legal entity - the testing laboratory shall carry out the sourse and validated air quality monitoring data and air pollution report and air quality assessment to the competent administrative body of the County, City of Zagreb and the city by 31th March of the current year for the previous calendar year.
  The competent authority of the counties, the City of Zagreb and the cities shall submit the Agency with original and validated data and air pollution reports and air quality assessment by 30th April of the current year for the previous calendar year.

## Slide 49: 13.4 DATA SUBMISSION DYNAMICS
Local Networks (JRS and JLS) – reports examples
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia

## Slide 50: 13.4 DATA SUBMISSION DYNAMICS
Local Networks (JRS i JLS)
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia
  The legal entity - the testing laboratory carrying out the measurements for the pollutant shall submit original and validated air quality monitoring data and air pollution report and air quality assessment to the competent administrative body of the County, City of Zagreb and by March 31th of the current year for the previous calendar year.
  The competent authority of the counties, the City of Zagreb and the cities shall submit to the Agency with source and validated data and air pollution reports and air quality assessment by April 30th of the current calendar year for the previous calendar year.

## Slide 51: 13.4 DATA SUBMISSION DYNAMICS
Local Networks (Polluter) – reports examples
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia

## Slide 52: 13.4 DATA SUBMISSION DYNAMICS
Local Networks - measurements of special purpose Article 33. Air Protection Act
Energy Research and Environmental Protection Institute
European Union IPA 2013 Programme for Croatia
  Art. 34. Air Protection Act and Art. 23. Ordinance define reporting only for measurements in accordance with Art. 31 and 32 and omits measurements of special purpose according to Art. 33.
  Even in Part XIII, INSPECTION SURVEILLANCE is not explicitly described as to who controls the measurement or reporting of these measurements.
  There are no such reports on Agency’s pages

## Slide 53: THANK YOU FOR YOUR ATTENTION
  Disclaimer: The contents of this publication are the sole responsibility of EKONERG – Energy Research and Environmental Protection Institute, Ltd. and can in no way be taken to reflect the views of the European Union
This project is funded by the European Union
Energy Research and Environmental Protection Institute